## Slide 1: Control of robotic arm with spiking neural networks
Projektpraktikum Computational Neuro Engineering 2017SS
Meng Wang, Bo Huang, Zhiwei Han
Image: References (left to right):
1) https://pixabay.com/de/sicherheit-wort-laser-modern-574079/ 2) https://pixabay.com/de/sicherheit-sicherheitskonzept-augen-1163108/
3) https://pixabay.com/de/objektiv-linse-null-eins-bin%C3%A4r-1278493/ 4) https://pixabay.com/de/sicherheit-wort-laser-modern-574079/

## Slide 2: Content
Introduction and Motivation
Goals and Steps
Project Plan and Distribution of Workload

## Slide 3: Content
Introduction and Motivation
Goals and Steps
Project Plan and Distribution of Workload

## Slide 4: Introduction and Motivation
Point its weapons (i.e. robot arm) only towards hostile intruders
Welcome allies with a friendly greeting
Emulation pre-calculated distance
Implement the procedure using spiking neural network based reinforcement learning algorithm (potentially Q-Learning)
Overall goal: finding a policy that allows the robot to reach a specific region through massive self learning
What
Detection and tracking are important problems in autonomous systems
Using spiking neural network based reinforcement learning approach we can achieve more complex or dynamic behavior
Why
Image: https://pixabay.com/de/idee-antwort-erleuchtung-klugheit-1026393/

## Slide 5: Content
Introduction and Motivation
Goals and Steps
Project Plan and Distribution of Workload

## Slide 6: Overall goal: Acting properly
Construction and Transformation of world coordinate to relative coordinate
Algorithm research
  Localization through pseudo-localization algorithm
  Create the penalty schema
Algorithm Testing and Implementation
Modelling Task
Mathematical Model and object localization
State and action space formulation
Reward design
Learning Algorithm and Implementation
Simulation (Mathematical model + Nengo)
Reinforcement Learning Task
Finding optimal policy
Mechanics and Control
Transfer of Algorithms on real robot arm
Modelling the uncertainty
Performance Evaluation
Practical Implementation
Making Robot
what the simulator does
Subgoal
Tasks and Steps
Reward
Action
State

## Slide 7: Content
Introduction and Motivation
Goals and Steps
Project Plan and Distribution of Workload

## Slide 8: Project plan - visualized using a Gantt-Chart
May
Jun
Jul
19
20
21
21
22
23
24
25
26
27
28
Test & Implementation
Final
Presentation
21.07.2017
Test on Robot
Evaluation & Refinement
Project
Plan
Presentation
12.05.2017
Discussion
02.06.2017
Discussion
19.05.2017
Intermediate
Document-
ation
23.06.2017
Project
Progress
presentation
09.06.2017
Activity
Discussion
16.06.2017
Meetings, Reports
and Milestones
Algorithm research
Simulation
Mechanical Fixes
Status
Learning Algorithm
Pre-final
Meeting
07.07.2017
State/action space
Week
Reward & Parameters
Documentation
Mathematical model
Organization
Modelling
Reinforcement
Learning
Implement practically
Discussion
26.05.2017
Discussion
14.07.2017
Discussion
30.06.2017

## Slide 9: Task distribution
Modelling
Reinforcement Learning
Practical Implementation
Step / Subtasks |  | Who | Deadline
Simulation Desgin |  |  | 
Write a python script that makes robot perform predefined movements taking measurement of the environment |  | W | 19/05
Generate the artificial states using the mentioned algorithm |  | B/M | 19/05
ALGORITHM RESEARCH |  |  | 
Search for distance extraction algorithm and the python APIs (coordinate transformation and relative distance etc.) |  | B | 19/05
Search for the construction and training schema for spiking neural network and a proper reinforcement learning algorithm |  | M | 19/05
TESTING AND IMPLEMENTAION |  |  | 
Find possibilities to implement these algorithms in python using APIs and libraries or write the code directly. |  | M/B/W | 26/05
Test the algorithms offline using artificial generated states |  | M/B | 26/05
Image: Reference: https://pixabay.com/de/umzug-tragen-schrank-treppe-hoch-1015581/

## Slide 10: Task Distribution
Modelling
Reinforcement Learning
Practical Implementation
Step / Subtasks |  | Who | Deadline
STATE AND ACTION SPACE FORMULATION |  |  | 
Create artificial states that will be used as input data to the simulator (the artificial states can be generated based on the measurement taken with robot and based on geometrical reasoning) |  | B/W | 02/06
LEARNING ALGORITHM AND IMPLEMENTATION |  |  | 
Create a python default template (i.e. import relevant modules, define spiking neural network and respective default values for actions, states, rewards, value function) to allow for simple coding. |  | W/B | 16/06
Create a function prototype for a function that returns an action according to a policy |  | M | 16/06
MATHEMATICAL SIMULATION |  |  | 
Try several learning algorithms with the predefined setup and make them run properly on simulator using the artificial states as an input sequence. |  | B/W/M | 16/06
Compare the different learning algorithms based on stability, robustness and speed in the simulator |  | B/W/M | 16/06
REWARD DESIGN |  |  | 
If necessary do an additional tuning of the rewards or the discount factor using the previously created functions. |  | B/W/M | 16/06
Image: Reference: https://pixabay.com/de/umzug-tragen-schrank-treppe-hoch-1015581/

## Slide 11: Task Distribution
Modelling
Reinforcement Learning
Practical Implementation
Step / Subtasks |  | Who | Deadline
TRANSFER OF ALGORITHMS ON ROBOT |  |  | 
Identify possible mechanical issues and create fixes (e.g. check the movement) |  | B | 30.06
MECHANICS AND CONTROL |  |  | 
Implement algorithm prototypes (Spiking neural network based Reinforcement learning) on robot and identify, if the performance/behavior largely deviates form the simulator |  | M/B/W | 07.07
PERFORMANCE EVALUATION |  |  | 
Evaluate the performance and possibly improve the algorithm using simulation and real robot. |  | M/B/W | 21.07
Image: Reference: https://pixabay.com/de/umzug-tragen-schrank-treppe-hoch-1015581/

## Slide 12: Task Distribution
Modelling
Reinforcement Learning
Practical Implementation
Documentation will be handled by all group members continuously but mainly from
01/07 to 14/07
Image: Reference: https://pixabay.com/de/umzug-tragen-schrank-treppe-hoch-1015581/
Step / Subtasks |  | Who | Deadline
TRANSFER OF ALGORITHMS ON ROBOT |  |  | 
Identify possible mechanical issues and create fixes (e.g. check the movement) |  | B | 30.06
MECHANICS AND CONTROL |  |  | 
Implement algorithm prototypes (Spiking neural network based Reinforcement learning) on robot and identify, if the performance/behavior largely deviates form the simulator |  | M/B/W | 07.07
PERFORMANCE EVALUATION |  |  | 
Evaluate the performance and possibly improve the algorithm using simulation and real robot. |  | M/B/W | 21.07

## Slide 13
BACKUP

## Slide 14: Module: Modelling
Result 1
Result 2
Result 3
Result 4
Result 5
Recent Results
Risk 1
Risk 2
Risk 3
Risk 4
Risk 5
Risks
Task 1
Task 2
Task 3
Task 4
Task 5
Upcoming Tasks
Subgoal / Step | Status
Modelling Goal 1 ………………………………… | 
Modelling Goal 1 ………………………………… | 
Modelling Goal 1 ………………………………… | 
Modelling Goal 1 ………………………………… | 
Modelling Goal 1 ………………………………… | 
BACKUP